CUI/Atd/31/Biotech (2020-2021)

| Sr. No. | Items Specifications | Required Quantity |
| --- | --- | --- |
| 01 | Ph Meter (Benchtop) Specifications Benchtop Can measure pH range from 0 - 14 LCd display Also show value in mV | 01 No |
| 02 | Indoor monitor for VOCs and formaldehyde Can monitor formaldehyde from indoor environment range from 0-4mg/m3. Can monitor total volatile organic compounds (TVOCs) including benzene from indoor environment range from 0 -12 mg/m3 LCD display With rechargeable Battery and charger | 01 No |
| 03 | Orbital shaker Small size can hold 6-8 flasks 20-400 RPM Digital display Time control function | 01 No |
| 04 | Power Supply for electrophoresis Application for DNA/RNA electrophoresis, SDS-PAGE Two to four sets of output terminals for running of multiple electrophoresis unit Multiple programmable options Output range: 10 – 250 volts LCD display | 01 No |
| 05 | UV lamp Suitable for TLC analysis Have two UV lamps of 254 and 365 nm wavelength | 01 No |
| 06 | Gas Tight Syringe Suitable for sampling of gases Capacity 3-15 ml Made of glass and Teflon Can lock the gasses inside syringe | 01 No |